 Installation and configuration

# 1 Raspberry PI Basics
## 1.1 Raspberry PI Model
Install software on a Raspberry PI 4; check the Raspberry PI model with:
$ cat /proc/cpuinfo | grep Model

## 1.2 Installing the OS
Insert a 32 Gbyte SD Card into a card reader, connect it to your PC and execute the Raspberry PI Imager to install the OS.
Read Installing the Operating System
## 1.3 Enabling Remote Connection
We want to work remotely through a wireless connection on the Raspberry PI via SSH and VNC. Raspberry PI Networking Instructions
We need Wi-Fi SSID and password here to configure a VNC connection.
Previous versions of Raspberry Pi OS supported client connections from RealVNC. In Raspberry Pi OS Bookworm or later, RealVNC is no longer supported. Instead, you can connect using TigerVNC. RealVNC is OK and its UI is much more user friendly than the TigerVNC one.
Raspberry PI credentials : pi / rpigb
## 1.4 Configuring the IQaudIO DAC+ Board
The config.txt file
Edit the /boot/firmware/config.txt file:
# For more options and information see
# http://rptl.io/configtxt
# Some settings may impact device functionality. See link above for details

# Uncomment some or all of these to enable the optional hardware interfaces
#dtparam=i2c_arm=on
#dtparam=i2s=on
#dtparam=spi=on

# Enable audio (loads snd_bcm2835)
#dtparam=audio=on

# Additional overlays and parameters are documented
# /boot/firmware/overlays/README

# Automatically load overlays for detected cameras
#camera_auto_detect=1

# Automatically load overlays for detected DSI displays
display_auto_detect=1

# Automatically load initramfs files, if found
auto_initramfs=1

# Enable DRM VC4 V3D driver
dtoverlay=vc4-kms-v3d
max_framebuffers=2

# Don't have the firmware create an initial video= setting in cmdline.txt.
# Use the kernel's default instead.
disable_fw_kms_setup=1

# Run in 64-bit mode
arm_64bit=1

# Disable compensation for displays with overscan
disable_overscan=1

# Run as fast as firmware / board allows
arm_boost=1

# load IQAUDIO device drivers
dtoverlay=iqaudio-dacplus

[cm4]
# Enable host mode on the 2711 built-in XHCI USB controller.
# This line should be removed if the legacy DWC2 controller is required
# (e.g. for USB device mode) or if USB support is not required.
otg_mode=1

[all]

## 1.5 Configuring the Volume Rotary Encoder
The IqaudIO DAC+ pre-amplifier volume is controlled by a rotary encoder.
A Python script (/home/pi/b3_clone/rpi/monitor-volume.py) is used to monitor the volume rotary encoder; it uses the gpiozero library and amixer command calls.
Read the paragraph 17 of the IQaudIO-User-Guide.pdf document about the rotary encoder.
Use Visual Studio on Linux Desktop in SSH mode to edit the Raspberry PI Python code remotely.
## 1.6 Executing Code on Startup
### /etc/rc.local
This file is used to execute code on Raspberry PI startup.
#!/bin/sh -e
#
# rc.local
#
# This script is executed at the end of each multiuser runlevel.
# Make sure that the script will "exit 0" on success or any other
# value on error.
#
# In order to enable or disable this script just change the execution
# bits.
#
# By default this script does nothing.

# Print the IP address
_IP=$(hostname -I) || true
if [ "$_IP" ]; then
  printf "My IP address is %s\n" "$_IP"
fi

exec 2> /tmp/rc.local.log # send stderr from rc.local to a log file
#exec 1>&2 # send stdout to the same log file
set -x # tell sh to display commands before execution

export DISPLAY=:0
export $(dbus-launch)

# launch setBfree and all necessary stuff to perform MIDI connections
su - pi /usr/bin/runb3

exit 0

#

### runb3
This script has to be copied to /usr/bin.
#!/bin/bash
# runB3
#
export HOME="/home/pi"
export DISPLAY=:0

# Wait for the Arduino boards to be present
counter=0
while [ ! -e /dev/b3_keyboards ]; do
    sleep 1s
    counter=$((counter + 1))
    if [ $counter -ge 10 ]; then
        exit
    fi
done
printf "/dev/b3_keyboards\tOK\n\n"

counter=0
while [ ! -e /dev/b3_pedals ]; do
    sleep 1s
    counter=$((counter + 1))
    if [ $counter -ge 10 ]; then
        exit
    fi
done
printf "/dev/b3_pedals\t\tOK\n\n"

counter=0
while [ ! -e /dev/b3_controls ]; do
    sleep 1s
    counter=$((counter + 1))
    if [ $counter -ge 10 ]; then
        exit
    fi
done
printf "/dev/b3_controls\tOK\n\n"

counter=0
while [ ! -e /dev/b3_drawbars ]; do
    sleep 1s
    counter=$((counter + 1))
    if [ $counter -ge 10 ]; then
        exit
    fi
done
printf "/dev/b3_drawbars\tOK\n\n"

sudo chmod 666 /dev/b3_keyboards
sudo chmod 666 /dev/b3_pedals
sudo chmod 666 /dev/b3_controls
sudo chmod 666 /dev/b3_drawbars
printf "/dev/b3_* chmod\t\tOK\n\n"

# exit here if you have to upgrade Arduinos firmware
# to setBfree and therefore unusable for firmware update.
# do not forget to comment this out afterwards
#exit 0
#

# ttymidi creates ALSA MIDI input and output ports
# the PMK25H pedal board is controlled by an Arduino Leonardo
# which enumerates natively as an ALSA MIDI device; no need for ttymidi for pedals
/usr/local/bin/ttymidi -s /dev/b3_keyboards -n b3_alsa_midi_keyboards -v &
/usr/local/bin/ttymidi -s /dev/b3_controls -n b3_alsa_midi_controls -v &
/usr/local/bin/ttymidi -s /dev/b3_drawbars -n b3_alsa_midi_drawbars -v &
sleep 2s
printf "ttymidi\t\t\tOK\n\n"

# start the B3 emulator
/usr/bin/pw-jack /opt/setBfree/bin/setBfree &
sleep 2s
printf "pw-jack setBfree\tOK\n\n"

# Arduinos to setBfree connections are done by loading a patchbay config file
/usr/bin/qpwgraph --activated /home/pi/b3_clone/rpi/b3.qpwgraph &
sleep 2s
printf "qpwgraph\t\tOK\n\n"

# start the Raspberry PI UP dashboard app
/home/pi/.venv/bin/python /home/pi/b3_clone/rpi/b3_up_py/b3_up_gui.py &
sleep 2s
printf "Python dashboard\tOK\n\n"

# initialize drawbars and controls Arduinos
stty 115200 -F /dev/b3_drawbars
printf "D\n" > /dev/b3_drawbars
sleep 1s
stty 115200 -F /dev/b3_controls
printf "C\n" > /dev/b3_controls
sleep 1s
printf "Drawbars and Controls Arduinos initialized OK\n\n"

# Ready !
exit 0
# 2 RPI Display Settings
## 2.1 Activate X11
Wayland does not allow a 180° display rotation with a touch x,y inversion; we have to use the X11 window manager. This can be set by using raspi-config.
## 2.2 Rotate display and touchscreen
The Raspberry PI has to be rotated 180° in order to get the proper orientation for USB and power connectors towards Arduino boards and power supply.
If the screen is rotated, the touch input has to be rotated too.
1. From the Raspberry PI desktop, activate Start > Preferences > Screen Configuration
2. Right-click the DSI-1 screen
3. Set resolution to 800x480
4. Set orientation inverted
5. Select the proposed Touchscreen
## 2.3 Modify the config.txt file
Set the /boot/firmware/config.txt file content as follows:
# For more options and information see
# http://rptl.io/configtxt
# Some settings may impact device functionality. See link above for details

# Uncomment some or all of these to enable the optional hardware interfaces
#dtparam=i2c_arm=on
#dtparam=i2s=on
#dtparam=spi=on

# Enable audio (loads snd_bcm2835)
#dtparam=audio=on

# Additional overlays and parameters are documented
# /boot/firmware/overlays/README

# Automatically load overlays for detected cameras
#camera_auto_detect=1

# Automatically load overlays for detected DSI displays
display_auto_detect=1

# Automatically load initramfs files, if found
auto_initramfs=1

# Enable DRM VC4 V3D driver
dtoverlay=vc4-kms-v3d
max_framebuffers=2

# Don't have the firmware create an initial video= setting in cmdline.txt.
# Use the kernel's default instead.
disable_fw_kms_setup=1

# Run in 64-bit mode
arm_64bit=1

# Disable compensation for displays with overscan
disable_overscan=1

# Run as fast as firmware / board allows
arm_boost=1

# load IQAUDIO device drivers
dtoverlay=iqaudio-dacplus

[cm4]
# Enable host mode on the 2711 built-in XHCI USB controller.
# This line should be removed if the legacy DWC2 controller is required
# (e.g. for USB device mode) or if USB support is not required.
otg_mode=1

[all]

## 2.4 Making the mouse cursor invisible
Install unclutter :
$ sudo apt-get install unclutter

Create or edit ~/.xinitrc to add the following line :
unclutter -idle 0 &

# 3 setBfree
## 3.1 Downloading and installing setBfree

$ cd /Downloads
$ wget http://x42-plugins.com/x42/linux/setBfree-v0.8.12-5-arm64.tar.gz
$ sudo tar -xzvf setBfree-v0.8.12-5-arm64.tar.gz -C /opt
## 3.2 Configuring setBfree
On startup, setBfree is set up by two configuration files : default.cfg and default.pgm. Both files have to be copied to $HOME/.config/setBfree.
The settings defined in default.cfg are applied during the initialization phase of the program and remain unchanged, while default.pgm declares runtime parameters which can be applied at any time by the user.
Important parameters changes in default.cfg:
The most left PKM25H pedal plays a C2 (36) note instead of C1 (24). The necessary octave transposition is applied by setting:
midi.pedals.transpose=-12

Upper and lower keyboards, as well as pedals MIDI channels are set by:
midi.upper.channel=1
midi.lower.channel=2
midi.pedals.channel=3

MIDI controller program number offset:
pgm.controller.offset=0

# 4 PipeWire
The B3 clone Arduino boards (keyboards, pedalboard, drawbars and controls) have to be declared as MIDI peripherals and connected to setBfree as MIDI inputs. The setBfree audio outputs have to be connected to the IqaudIO DAC+ inputs. These software connections are done by using PipeWire.
Using PipeWire instead of PulseAudio makes the audio management on Raspberry PI easier and more reliable.
## 4.1 Installing and Configuring PipeWire
https://wiki.archlinux.org/title/PipeWire
Install Pipewire: Make sure you have Pipewire installed on your system. You can typically install it using your distribution's package manager. For example, on a Debian-based system, you might use:
$ sudo apt install pipewire

As mentioned in the above URL, files located under /usr/share/pipewire	should be copied to /etc/pipewire.
$ sudo cp /usr/share/pipewire/* /etc/pipewire/.

Install Pipewire Audio Modules: Pipewire provides various audio modules to handle different tasks. You'll likely need to install the necessary audio modules to support your hardware. For IQaudio DAC+, you might need modules related to ALSA (Advanced Linux Sound Architecture).
$ sudo apt-get -y install pipewire-audio
$ sudo apt-get -y install pipewire-alsa
$ sudo apt-get -y install pipewire-jack
$ sudo apt-get -y install pipewire-pulse

Install the Session Manager: PipeWire doesn’t have its own connection logic, so you have to install a session manager.
$ sudo apt install wireplumber

Install qpwgraph: it is used to display PipeWire blocks and make connections between them, like Qjackctl.
$ sudo apt-get -y install qpwgraph

Check pulseaudio-alsa installation and remove it if installed:
$ dpkg -L pulseaudio-alsa
$ sudo apt remove --purge --autoremove pulseaudio-alsa
$ sudo apt remove pulseaudio

Get Services Ready
$ systemctl --user --now disable pulseaudio.service pulseaudio.socket
$ systemctl --user mask pulseaudio
$ systemctl --user --now enable pipewire pipewire-pulse wireplumber
$ sudo reboot

1. Identify your DAC+ Card: Before configuring Pipewire, you need to know the identifier of your IQaudio DAC+ card. You can typically find this by running the aplay -l command, which lists all audio devices. Look for your DAC+ card in the list and note down its identifier, such as "hw:0,0".
2. Edit Pipewire Configuration: Pipewire configuration is typically done through configuration files. The main configuration file is usually located at /etc/pipewire/pipewire.conf. You'll need to edit this file to specify your IQaudio DAC+ card as the default audio output device.
$ sudo nano /etc/pipewire/pipewire.conf

Look for the [pipewire] section and add or modify the	following line to specify your DAC+ card:
default.clock.rate = 44100
default.clock.channels = 2
default.clock.format = s16le
default.clock.device = alsa_output.hw_0_0
1. Restart Pipewire: After making changes to the configuration file, you'll need to restart Pipewire for the changes to take effect. You can typically do this using the following command:
$ sudo systemctl restart pipewire
## 4.2 Running setBfree from PipeWire
$ pw-jack /usr/bin/setBfree &

# 5 ttymidi

ttymidi allows the Arduino Nano Every boards of the B3 clone to interface with ALSA MIDI applications. http://www.varal.org/ttymidi/
The PMK25H pedal board uses an Arduino Leonardo which enumerates as a MIDI device; therefore using ttymidi is not necessary on the /dev/b3_pedals device.
## 5.1 Building and installing ttymidi
Install libasound2
$ sudo apt install libasound2-dev

Build and install ttymidi
$ cd /tmp
$ wget http://www.varal.org/ttymidi/ttymidi.tar.gz
$ tar xvf ttymidi.tar.gz
$ cd ttymidi
$ make
$ sudo make install
Executable folder: /usr/local/bin
## 5.2 Using ttymidi
Do not use ttymidi on /dev/b3_pedals
$ /usr/local/bin/ttymidi -s /dev/b3_keyboards -n b3_alsa_midi_keyboards -v &
$ /usr/local/bin/ttymidi -s /dev/b3_controls -n b3_alsa_midi_controls -v &
$ /usr/local/bin/ttymidi -s /dev/b3_drawbars -n b3_alsa_midi_drawbars -v &
# 6 Assigning Static USB Ports Names
Our Arduino Nano Every based boards connect to the Raspberry PI USB ports. Once connected, they have names such as /dev/ttyACM[0-n]. To make the management of these serial ports easier, we want these names to be static:
- Keyboards :	b3_keyboards
- Pedals :	b3_pedals*
- Controls :	b3_controls
- Drawbars :	b3_drawbars
1. Connect only one USB device; the keyboards Arduino Nano Every, for example.
2. List the USB attributes for this device:
$ udevadm info --name=/dev/ttyACMx --attribute-walk

where x is a number matching the device port. In the attribute list, look for an	attribute that is unique for a device (check idVendor, idProduct and serial). We	have to use serial because we connect several Arduino Nano Every boards and	serial is unique.
../..
    ATTRS{product}=="Arduino Nano Every"
    ATTRS{quirks}=="0x0"
    ATTRS{remove}=="(not readable)"
    ATTRS{rx_lanes}=="1"
    ATTRS{serial}=="C9ACB9635151363448202020FF180D3E"
    ATTRS{speed}=="12"
    ATTRS{urbnum}=="10"
    ATTRS{version}==" 1.10"
../..

Create (or open) a rules file:
$ sudo touch /etc/udev/rules.d/99-usb-serial.rules

Insert the following line into this rules file:
KERNEL=="ttyACM*", ATTRS{product}=="Arduino Nano Every",	ATTRS{serial}=="C9ACB9635151363448202020FF180D3E", SYMLINK+="b3_keyboards"

Reload the udevadm rules:
$ sudo udevadm control --reload-rules

Disconnect, then reconnect the keyboards Arduino board and type:
$ ls /dev/b3*

Repeat the operations for the others Arduino devices.

* The pedalboard is controlled by an Arduino Leonardo which has no serial number; the product name is used to identify this board.
# 7 Building Arduino Firmware Remotely
## 7.1 Install Arduino CLI on Raspberry PI
$ curl -fsSL https://raw.githubusercontent.com/arduino/arduino-cli/master/install.sh | sh
$ nano ~/.bashrc

Append the following line :
export PATH=$PATH:/home/pi/bin
$ sudo reboot
We can build every Arduino B3 project locally (on Linux desktop), then upload the binary to the Arduino from the Raspberry PI. This 3-step build process allows firmware updates without removing the boards from the organ and can be scripted as follows:
#!/bin/bash
# controls_remote_build

arduino-cli compile -b arduino:megaavr:nona4809:mode=off --output-dir=./bin

sshpass -prpigb scp bin/* pi@192.168.0.31:~/b3_clone/arduino/controls

sshpass -prpigb ssh pi@192.168.0.31 '/home/pi/bin/arduino-cli upload -b arduino:megaavr:nona4809:mode=off -p /dev/b3_controls
–input-dir=/home/pi/b3_clone/arduino/controls'

The same can be done for drawbars and keyboards.
# 8 Connecting Arduinos MIDI Outputs to SetBfree
Use qpwgraph to graphically connect Arduinos MIDI outputs to setBfree, then save the patchbay connections to /home/pi/b3_clone/rpi/b3.qpwgraph
qpwgraph will be launched by the /usr/bin/runb3 script as follows:
$ /usr/bin/qpwgraph -a -m /home/pi/b3_clone/rpi/b3.qpwgraph &
# 11 Software Development
## 11.1 Raspberry PI Software
The Raspberry PI software:
- displays registration selection
- sends registration selection data to the drawbars firmware
- communicates with setBfree (volume, reverb, overdrive) through virtual MIDI port
The Raspberry PI software is written in Python; the source files are located on the Raspberry PI and edited with the Visual Studio Code IDE installed on the desktop. VSC works remotely on the RPI through an SSH connection on: 192.168.0.31 (the RPI IP address).
The Python source code relies on some packages which are relevant on a RPI , but not on a desktop: gpiozero and alsaaudio.
### Creating a Python virtual environment
Create and activate a Python virtual environment on the Raspberry PI:
$ cd /home/pi
$ python3 -m venv .venv
$ source .venv/bin/activate
### Installing Python Packages
$ /home/pi/.venv/bin/pip install customtkinter	nice looking GUI
$ /home/pi/.venv/bin/pip install pillow	images
$ /home/pi/.venv/bin/pip install pyserial	serial communication
$ /home/pi/.venv/bin/pip install gpiozero	rotary encoders
$ /home/pi/.venv/bin/pip install alsaaudio	control the alsa mixer
$ /home/pi/.venv/bin/pip install mido[ports-rtmidi]	MIDI virtual port

The lgpio located in the venv produces warnings which can be removed by copying the regular python3 lgpio to the venv.
### Selecting the Python Interpreter
1. On VS Code (on the desktop), execute ctrl+shift+P
2. In the command window, type select interpreter
3. Select the .venv interpreter
## 11.2 Arduino Nano Every Firmware
Arduino firmware is flashed on the following boards (the pedalboard firmware was developed by PedaMidiKit) :
- keyboards (ArduinoB3Keyboards project)
- drawbars (ArduinoB3Drawbars project)
- main panel controls (ArduinoB3Controls)
These are C++ projects developed on the desktop with Visual Studio Code and its PlatformIO extension. The Arduino source files are located on desktop and the projects are built locally, then the HEX file is sent to the Raspberry PI which in turn flashes the Arduino firmware. This tool chain allows remote in-system organ firmware update.
USB ports have to be available for the firmware update process to perform properly : do not forget to temporarily modify the /usr/bin/runb3 script by uncommenting the “exit 0” line.
### PlatformIO Core (CLI)
PlatformIO Core has to be installed on the Raspberry PI to allow remote operations such as firmware update or running unit tests on the Arduino boards.
To download PlatformIO Core on the Raspberry PI, type:
$ cd /home/pi
$ wget -O get-platformio.py https://raw.githubusercontent.com/platformio/platformio-core-installer/ master/get-platformio.py

Then, install PlatformIO with:
$ python3 get-platformio.py
$ /home/pi/.platformio/penv/bin/pio account login
$ enter credentials: Georgie-Nantes password is in Bitwarden vault
$ /home/pi/.platformio/penv/bin/pio remote agent start &

In Visual Studio Terminal, check that the Raspberry PI is in the agents list:
$ pio remote agent list
b3pi4

$ pio remote device list
Agent b3pi4
===========
/dev/ttyACM0
------------
Hardware ID: USB VID:PID=2341:0058 SER=45CF82F551514C4630202020FF0E2645 LOCATION=1-1.1:1.0
Description: Arduino Nano Every

/dev/ttyACM1
------------
Hardware ID: USB VID:PID=2341:0058 SER=3D4768A751514C4630202020FF0D4243 LOCATION=1-1.2:1.0
Description: Arduino Nano Every

/dev/ttyACM2
------------
Hardware ID: USB VID:PID=2341:0058 SER=C9ACB9635151363448202020FF180D3E LOCATION=1-1.3:1.0
Description: Arduino Nano Every

/dev/ttyACM3
------------
Hardware ID: USB VID:PID=2341:8036 SER=MIDI LOCATION=1-1.4:1.0
Description: Arduino Leonardo

To build an Arduino project from desktop VSC, activate the PlatformIO extension and run General > Build
To update an Arduino firmware from desktop VSC, activate the PlatformIO extension and run Remote > Remote Upload
# 12 Troubleshooting
## 12.1 Startup
Examine /tmp/rc.local.log
## 12.2 MIDI
Checking MIDI messages coming from Arduinos
The following instructions refer to the b3_controls Arduino board, but they can be appplied to the b3_drawbars and b3_keyboards ones as well.
SSH connect to the Raspberry PI from the Linux desktop
$ ssh pi@192.168.0.31

install midisnoop on the Raspberry PI
$ sudo apt-get update
$ sudo apt-get -y install midisnoop

set terminal line for b3_controls Arduino
$ stty 115200 -F /dev/b3_controls

launch midisnoop and execute Edit > Configure
$ midisnoop &

reset the b3_controls board
On reset, the Arduino enters the setup() function, in which it waits for the ‘C’	character (C for b3_controls and D for b3_drawbars) before executing the loop()	function.
$ printf "R\n" > /dev/b3_controls
$ printf "C\n" > /dev/b3_controls

The loop() function executes and sends MIDI Program Change messages	corresponding to switches positions and Control Change messages corresponding	to the expression pedal position. All MIDI messages can be observed in the	midisnoop window.

## 12.3 Audio
Launch alsamixer and select IqaudIODAC sound card.